## Slide 1: Hiwonder JetAuto LiDAR SLAM
Rodolfo Andrés Rivas Matta, PhD Candidate
Notes: Hello, everyone! My name is Rodolfo, and I will be presenting my term project: implementing SLAM with a 2D LiDAR sensor in a Hiwonder JetAuto robot—of which I will show some pictures later.

## Slide 2: Agenda
Introduction
Problem Formulation
Implementation Details & Demonstration
Evaluation and Conclusion
Q&A
Notes: Here is the agenda for the presentation, so let’s get right into it!

## Slide 3: Introduction
Task description and motivation:
Simultaneous Localization And Mapping (SLAM) is critical for autonomous driving.
SLAM allows systems to move while keeping track of their position and environment.
This project attempts to implement and demonstrate a real-world application of SLAM.
It will serve as a baseline for future research.
Notes: First, let’s understand what the task is about and the motivation behind it.
SLAM is an acronym that stands for Simultaneous Localization and Mapping, which is a critical task for autonomous driving. It allows bots to plan and navigate, always keeping track of their position.
As it is an essential task for autonomous systems, like self-driving cars, it seemed appropriate for a term project in an intelligent autonomous robotics class.
However, there is another motivation behind this specific project. My dissertation advisors recently published a paper about a new approach to machine perception during motion. Their method allows to perform 3-D mapping and capturing the camera heading only with a sequence of 2-D the images; it does not use any kind of stereos cameras. The method is new, and there are not many studies that compare it with other standard approaches.
Hopefully, this project will evolve and serve as a baseline to compare that new approach in tasks like obstacle avoidance.

## Slide 4: Problem Formulation
Robot: Hiwonder JetAuto Pro
Inputs:
  2D LiDAR data.
2-Parts Task:
  Part 1: Mapping.
    Manual remote-control navigation.
    Create a 2D map of a room.
  Part 2: Autonomous Driving.
    Load the 2D map created in part 1.
    User must specify the robot’s 2D pose.
    User select points in the map → robot navigates to them.
Project uses robot’s sensors and ROS1.
The robot also comes with manufacturer’s ROS launch files.
Notes: Let’s get back to this project and discuss the tasks, constraints, and assumptions.
I am using a Hiwonder JetAuto Pro. That is a four-wheeled robot with a 2D LiDAR, one camera, and a robotic arm; it is computationally powered by a Jetson Nano. It is an older generation, so it uses ROS1 and Ubuntu 18. For this project, the arm and the camera remain offline; the final implementation only uses the LiDAR for mapping and wheels for movement.
The initial proposal had two sets of tasks. The first set is described here as a two-part task. The second set built on the first one, by replacing the manual driving during mapping with autonomous exploration using AR tags (Augmented Reality tags or markers). However, that was only going to be the case if time allowed, and it didn’t allow. Therefore, I will focus only on the first set of tasks here.
The first set is made up of two parts. The first part is about generating a map, which is done with some SLAM algorithm, that I will describe later, and manually driving the robot.
The second part consists of loading the 2-D generated the map, configuring the robot starting point, its location and heading, and selecting points in the map so that the robot autonomously drives to them. That’s the goal.
Limitations? Using only the LiDAR and wheels, and operating within Ubuntu 18 and ROS1, which both have been discontinued. Assumptions? I can use any ROS built-in command or tool, or any manufacturer ROS launch file.

## Slide 5: Implementation Details and Demonstration: Overview
Communication Setup
Notes: With that, let’s get into the implementation details and demonstration.
Briefly, though, I would like to discuss my communication set up. As it is common in robotics, this bot broadcasted its own Wi-Fi network without being connected to the internet. Additionally, I was mainly working from a Mac computer. To make my life more comfortable, and still being able to connect to the internet to get any help while troubleshooting, I had intermediaries between my computer and the bot.
During the first few stages, while I was working on configuring the bot, I had an Orange Pi that will receive connections from a specific domain and had a secondary network interface connected to the robot. Then, I would use the Pi as a proxy to connect to the robot while I was away from home.
In later stages, when I wanted to use some ROS built-in tools, I set up a virtual machine with Ubuntu 18 and ROS1 that connected to the robot through a secondary USB Wi-Fi dongle.
In both cases, I could quickly switch between sending commands to the robot and open tabs to look up how to fix errors, meaning my workflow was basically just making mistakes at the speed of light.

## Slide 6: Implementation Details and Demonstration: Overview
Part 1 Tasks
  Start the built-in roslaunch jetauto_slam slam.launch command.
    Default flag (with odom): slam_methods:=gmapping
    Without odom: slam_methods:=hector
    Starts up map server.
  Use teleop_twist_keyboard generic ROS node.
  Save the map: rosrun map_server map_saver -f ~/jetauto_ws/src/jetauto_slam/maps/map_name map:=/jetauto_1/map
Notes: When the communication was set up, and after days configuring the robot, these are the steps I used to generate a map.
I did end up using a ROS launch file provided by the manufacturer, but my robot is old and was not in perfect conditions. First, I used the gmapping package, which generates a map using LiDAR scans and the wheels odometry. Unfortunately, one, and now two, of the wheels had stripped screw holes; in other words, the controller would send commands to move forward, the motors would move, but the wheels would stay static, resulting in wrong measurements from the odometry.
Then, I moved to using Hector SLAM. That is a similar mapping algorithm, but it only relies on LiDAR scans. That allowed me to generate more accurate maps, even when the robot would drift to its left side, under one condition: I must drive slower. This algorithm will stitch together different scans with enough overlap.
So, I launched the mapping algorithm, manually drove the bot around the room, and finally saved the map through the map server node.
Part 1, completed. You can see the generated map on the left and some pictures of the room on the bottom right, including that long hallway.

## Slide 7: Implementation Details and Demonstration: Overview
Part 2 Tasks
  Foxglove Studio: https://foxglove.dev/home
  Run built-in launch command: roslaunch jetauto_navigation navigation.launch map:=map_name
  RViz (ROS Visualizer)
  RQT Reconfigure (ROS Qt-based GUI)
Adaptive Monte Carlo Localization
Global Path Planning: Dijkstra (default)
Local Costmap 2D
Notes: Part two consists of autonomous driving using the generated map in part one.
Again, I used a launch file provided by the manufacturer, that took the map that I previously generated as an argument. In my remote computer, I will use the ROS Visualizer, RViz, and the ROS Qt-based GUI Reconfigure tool, RQT reconfigure.
Let’s just say the first attempt didn’t fail; it just aggressively managed my expectations for the rest of the project.
Once RViz was up, I had to configure the map, laser scans, and the estimate 2-D pose. With that information, the robot was ready to get to a 2-D goal I specified. I fixed some parameters, like lowering the max speed or distrusting the odometry measurements for better accuracy, using the RQT reconfigure tool.
The robot would move autonomously using the Adaptive Monte Carlo Localization algorithm built in the system and used the Dijkstra algorithm for path planning to get to the goal. The robot would additionally, keep a local costmap for threats, or changes, during navigation. These are not parameters I configured, but I read these are the defaults for the packages I used.

## Slide 8: Implementation Details and Demonstration: Video
Notes: With that in mind, let’s admire this video demonstration.

## Slide 9: Implementation Details and Demonstration: Resources
ROS Melodic Wiki Documentation: https://wiki.ros.org/melodic/
  gmapping package.
Built-in Modules
Google Gemini
Documentation
Project Page: https://rodolfo.pro/project/slam-autonomous-nav.html
GitHub Repository: https://github.com/RARM/robotics-autolidar-hiwonder
Notes: What resources I used?
The ROS Melodic Wiki Documentation website, for example, when learning about packages,
I navigated through the source code of the manufacturer-provided packages, when trying to understand the parameters and requirements,
and Google Gemini, which was great for asking it, “why is it doing that?!” at 2 in the morning.
Additionally, I documented this project in my personal website. Here is the link.
And, to make the compilation of documentation easier at the end, and since I plan on working with this robot for the next semester, I documented major steps and findings in this separate open-source repository. Right here.

## Slide 10: Evaluation and Conclusion
The project was successful!
Limitations and Areas of Improvement
Autonomous navigation for initial mapping.
Outdated software (ROS and OS).
Replacement of loose wheels.
Recall there are plans to use it in future research.
Notes: Finally, did it execute the proposed functionality? Yes, it was successful.
Limitations and areas of improvement? A bunch, of course, but here I list a few.
First, finding a way to make it autonomously drive during the first part: generating the map.
Update the software; although, I don’t think that may be possible with this specific robot.
Definitely, I should replace the faulty wheel.
And, eventually dominate the world with this bot.
Don’t forget, I also plan to add other functions when I work on it next semester.

## Slide 11: THANK YOU
Notes: And th-th-th-that's all, folks! Any questions?